## Slide 1
Review 1.2
B. Tech. Project (19ECE495)
Batch ID: 070
Mutual coupling reduction in MIMO Patch Antenna Array for Wi-Fi and Bluetooth applications
MENTOR: : Ms. V. MEKALA DEVI
Dept. of Elec. and Commn. Engg.
Amrita School of Engineering, Coimbatore
CB.EN.U4ECE22225 | - | J Rohith
CB.EN.U4ECE22262 | - | Peddakudala Yashwanth
CB.EN.U4ECE22213 | - | Chundupalle Tej Siddanth

## Slide 2
Summary :
1.Project Focus: Design and implementation of a compact MIMO patch antenna array at 2.4 GHz with decoupling structures for Wi-Fi and Bluetooth applications, aiming for high isolation (>20 dB) and element spacing < λ/2..
2. Motivation:
Rising demand for MIMO systems in IoT, 5G, and smart devices.
3.Problem and objective:
Problem: Mutual coupling between closely spaced MIMO antenna elements reduces efficiency, gain, and matching.
Objective: Design, analyse, and prototype a patch antenna array with effective decoupling to enhance isolation while maintaining compactness at 2.4 GHz.

## Slide 3
Review | Month | Milestone
TIMELINE:
1.1 | June-July 2025 | Literature survey for decoupling structures
1.2 | August – September 2025 | Design and analysis of base antenna at 2.4 GHz.
1.3 | October-November 2025 | Design and analysis of a Patch antenna array at 2.4 GHz
2.1 | December 2025-January 2026 | Design and analysis of a Patch antenna array with decoupling structures at 2.4 GHz.
2.2 | February-March 2026 | Prototype and Measurement

## Slide 4: LITERATURE:
Sl. # | Title of the paper | Source | Inferences
1 | Compact Self-Isolated Four-Element MIMO Antenna for WLAN and ISM Bands Application | IEEE Antennas and Wireless Propagation Letters, 2023 | Key Advantage of Proposed Work Self-isolation (no extra structures). Most compact (40 × 40 mm²) among compared works. Highest isolation (>20 dB) and lowest ECC (<0.02). Very good for portable WLAN/ISM devices. Limitations Single-band (2.4 GHz) only. Lower gain (~2.8 dBi) compared to some dual/tri-band designs.
2 | Decoupling Between Extremely Closely Spaced Patch Antennas by Mode Cancellation Method | IEEE Antennas and Wireless Propagation Letters, 2024 | Key Advantage of Proposed Work Isolation: 5 dB → 15.4 dB+ (2.39–2.53 GHz). Better radiation: Gain 7.8 dBi, FBR 25 dB, low x-pol. High efficiency (82–87%), ECC < 0.004. Works for 1-D & 2-D arrays, simple + tiny size. Limitations Only good for very strong coupling (tiny gaps). Weak coupling → poor effect. Bandwidth small (~5%) unless modified.

## Slide 5: LITERATURE
Sl. # | Title of the paper | Source | Inferences
3 | Mutual Coupling Reduction of a Dual-Band Four-Port Patch Antenna With Co-Polarized Radiation Pattern by Controlling Electric Fields | IEEE Transactions on Antennas and Propagation, 2023 | Key Advantage of Proposed Work First dual-band, four-port, co-polarized patch antenna with low MC (< –15 dB) and single radiator. Compact + no extra feeding network. Limitations More design complexity (multiple pins + slots). Upper-band initially had non-broadside beam (fixed using pin 4). Bandwidth moderate compared to some wideband arrays.
4 | A Compact Multifrequency Broadband Dual-Antenna System With Mutual Coupling Reduction for Wi-Fi 6E Application | IEEE Transactions on Antennas and Wireless Propagation, 2024. | Key Advantage of Proposed Work Most compact design (shortest length). Achieves highest isolation (>22 dB). Covers all Wi-Fi bands including 6E (2.4 / 5 / 6–7 GHz). Maintains low ECC (<0.3) → better MIMO performance. Limitations Efficiency (40–50%) lower than some larger designs. Only dual-antenna system (not 4×4/8×8 scalable).

## Slide 6
Sl. # | Title of the paper | Source | Inferences
5 | Mutual Coupling Reduction in Dual-Band MIMO Antenna Using Parasitic Dollar-Shaped Structure for Modern Wireless Communication | IEEE Transactions on Antennas and Propagation, September 2023 | Key Advantage of Proposed Work Highest isolation (>30 dB) among compared designs. Lowest ECC (<0.02) → excellent diversity. Simple parasitic structure, compact design. Performance: Operating bands: 3.5 GHz (5G) and 5.2 GHz (WLAN). Isolation improved to >30 dB (without needing complex decoupling networks). Limitations Only dual-band (3.5 & 5.2 GHz). 2-element system (not tested for 4-port or higher). Moderate gain (~3.5 dBi) compared to some multi-port systems.
LITERATURE:

## Slide 7
Methodology:
7
Designing a Rectngular a Patch Antenna using HFSS
Experimental Validation of final results and Documentation
Fabrication of Optimized Design
Insertion of Decoupling Structure and Performance Analysis (Isolation,Gain)
Analysis of S Parameter , Gain plots for an element with HFSS
Design of 1×2 MIMO Array without Decoupling Structure
28-08-2025

## Slide 8
1) Designing a Microstrip Patch Antenna using HFSS
Antenna Dimension Calculation:
As the frequency of the application is 2.4GHz , considering Rogers RT duroid 5880 (εr = 2.2) as the suitable
substrate, the basic patch antenna dimensions are calculated below.
Ground Plane and Substrate Design:
Ensure the ground plane is at least 6 times the substrate height larger than the patch to provide optimal radiation efficiency and minimize fringing effects.
Simulation Setup in HFSS:
  Define the boundary conditions for the patch and ground plane using "Perfect E" boundaries.
  Assign a radiation boundary to a box surrounding the antenna, positioned at least λ/4 away from the structure to simulate the radiation in a free space environment.
  Apply the appropriate excitation, such as a Wave Port/Lumped Port.

## Slide 9
Patch Antenna Dimension Calculation:
As the frequency of the application is 2.4 GHz, considering Rogers RT duroid 5880 (εr = 2.2) is a suitable substrate, the basic patch antenna dimensions are determined through mathematical calculations.
Designed for 2.4 GHz rectangular patch on Rogers RT duroid 5880(εr = 2.2) with h = 1.6 mm.
Determining Path Widh(W) an Length(L)
Width
Effective Permittivity εeff​
Fringing extension ΔL
Fig: Simulated model of unit element of an Array
W= 49.38 mm
εeff≈2.03

## Slide 10
Impedance Matching:
Here, the length is λ/4 and the width can be calculated as follows:

## Slide 11
Methodology:
11
Designing an Element Microstrip Patch Antenna using HFSS
Experimental Validation of final results and Documentation
Fabrication of Optimized Design
Insertion of DecouplingStructure and
Performance
Analysis(Isolation,Gain)
Analysis of S Parameter , Gain plots for an element with HFSS
Design of 1×2 MIMO Array without Decoupling Structure

## Slide 12
Analysis of Patch Antenna with HFSS
Performance Evaluation: Simulate the design to obtain the key performance metrics, such as
S-parameters (S11)
Radiation pattern
Impedance characteristics
Gain
Efficiency; to optimize antenna performance for the desired application.
Fig: Obtained S(1,1) Plot

## Slide 13
Parameter | Unit Element
S(1,1) Parameter | -27.33dB
Gain | 4.42dB
Impedance Matching | 50.2Ω
Results

## Slide 14
Deliverables:
Review 1.2
14
Design and simulation of a unit element at 2.4 GHz rectangular patch antenna using substrate (εr = 2.2).
Analysis of S-parameters, impedance matching, and radiation characteristics of the antenna element
28-08-2025

## Slide 15: REFERENCES:
[1] G. Yang, Y. Zhang, and S. Zhang, “Compact Self-Isolated Four-Element MIMO Antenna for WLAN and ISM Bands Application ,” IEEE Open J. Antennas Propag., vol. 2, pp. 203–213, 2023, doi: 10.1109/OJAP.2023.3057062.
[2] W.-L. Zhou, S.-W. Qu, M. Xia, and S. Yang, “Decoupling Between Extremely Closely Spaced Patch Antennas by Mode Cancellation Method ,” IEEE Trans. Antennas Propag., vol. 70, no. 11, pp. 10475–10484, Nov. 2024, doi: 10.1109/TAP.2024.3195454.
[3] A. Li, S.-W. Qu, and S. Yang, “ Mutual Coupling Reduction of a Dual-Band Four-Port Patch Antenna With Co-Polarized Radiation Pattern by Controlling Electric Fields ,” IEEE Antennas Wireless Propag. Lett., vol. 21, no. 9, pp. 1762–1766, Sept. 2022, doi: 10.1109/LAWP.2022.3179404.
[4] Y. Yang, Y. Feng, L.-K. Zhang, Z. Xing, and J. Li, “ A Compact Multifrequency Broadband Dual-Antenna System With Mutual Coupling Reduction for Wi-Fi 6E Application ,” IEEE Antennas Wireless Propag. Lett., vol. 23, no. 12, pp. 4074–4078, Dec. 2024, doi: 10.1109/LAWP.2024.3428515.
[5] Z.-L. Su, K. W. Leung, and K. Lu, “Mutual Coupling Reduction in Dual-Band MIMO Antenna Using Parasitic Dollar-Shaped Structure for Modern Wireless Communication,” IEEE Trans. Antennas Propag., vol. 70, no. 9, pp. 7659–7669, Sept. 2023, doi: 10.1109/TAP.2023.3199567.

## Slide 16
Thank You
Review 1.2
16
28-08-2025