## Slide 1
Review 1.1
B.Tech Project (19ECE495)
Batch ID: 070
Mutual coupling reduction in MIMO Patch Antenna Array for Wi-Fi and Bluetooth applications
MENTOR: Ms. V. Mekaladevi
Dept. of Elec. and Commn. Engg.
Amrita School of Engineering, Coimbatore
CB.EN.U4ECE22225 | - | J Rohith
CB.EN.U4ECE22262 | - | Peddakudakla Yashwanth
CB.EN.U4ECE22213 | - | Chundupalle Tej Siddanth

## Slide 2: Outline
Problem Statement
Motivation
Objective
Deliverables
Novelty
Literature Survey
Methodology
References

## Slide 3
Problem Statement:
Design a Patch antenna array with decoupling structures at 2.4 GHz.
Challenge: In MIMO (Multiple-Input Multiple-Output) antenna systems, mutual coupling between closely spaced antenna elements significantly degrades system performance by:
Reducing antenna efficiency and gain.
Affecting impedance matching .
Goal: Achieving effective mutual coupling reduction while maintaining compact antenna array dimensions (less than λ/2 spacing) for 2.4 GHz Wi-Fi and Bluetooth applications.

## Slide 4
Motivation:
Growing Demand for MIMO Systems
•Wireless Communication Growth: Exponential increase in data traffic requires higher capacity and reliability.
•IoT and Smart Devices: Need for compact, efficient antennas in space-constrained devices.
•5G and Beyond: MIMO technology is fundamental for achieving high data rates
Technical Challenges.
•Miniaturization Requirements: Modern devices demand smaller antennas without performance compromise.
•Interference Issues: Dense deployment of wireless devices increases interference problems.
•Performance Optimization: Need for high isolation (>20 dB) while maintaining good radiation characteristics.

## Slide 5
Objectives:
Design and analysis of base antenna at 2.4 GHz.
Design and analysis of Patch antenna array at 2.4 GHz.
Design and analysis of Patch antenna array with decoupling structures.
Prototype and Measurement.
Performance Targets:
Isolation: > 20 dB between antenna elements
Element Spacing: < λ/2 for compact design
Operating Frequency: 2.4 GHz (Wi-Fi and Bluetooth bands)

## Slide 6
Milestones and Deliverables:
Review | Month | Milestone
1.1 | June-July 2025 | Literature survey for decoupling structures
1.2 | August – September 2025 | Design and analysis of base antenna at 2.4 GHz.
1.3 | October-November 2025 | Design and analysis of a Patch antenna array at 2.4 GHz
2.1 | December 2025-January 2026 | Design and analysis of a Patch antenna array with decoupling structures at 2.4 GHz.
2.2 | February-March 2026 | Prototype and Measurement

## Slide 7: Novelty
Compact Decoupling Structure Design: Propose a simple, compact decoupling structure that maintains antenna element spacing less than λ/2 while achieving high isolation (>20 dB).

## Slide 8: Literature :
S.No. | Title of the Paper | Source | Inferences
1 | Electric-Field Null Bending of a Single Dual-Port Patch Antenna for Colinear Polarization Decoupling Using Characteristic Modes Analysis | IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, 2022 | Operating Frequency: 5.4GHz Isolation:17 dB Antenna Spacing (Port-to-Port): 12.7 mm = 0.23λ₀ Method of Mutual Coupling Reduction: Electric-field null bending by combining two characteristic modes (TM₀₁ and TM₂₀) to create null points at the feeding locations of the opposite ports. Antenna Structure: Single Patch Antenna
2 | Mode-Counteraction Based Self-Decoupling in Circularly Polarized MIMO Microstrip Patch Array | IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, 2022 | Operating Frequency: 5.5GHz Isolation:59.4 dB Antenna Spacing (Center to Center): 21.64 mm = 0.4λ₀ Method of Mutual Coupling Reduction: Electric-field null bending Utilizes TM₁,₀ and TM₀,₁ modes to create null-field regions where feeding probes are positioned. Antenna Structure: 1×2 MPA Array

## Slide 9: Literature (continued):
S.No. | Title of the Paper | Source | Inferences
3 | A Compact Multifrequency Broadband Dual-Antenna System With Mutual Coupling Reduction for Wi-Fi 6E Application | IEEE ANTENNAS AND WIRELESS PROPAGATION LETTERS, 2024 | Operating Frequency bands:2.4–2.484 GHz(low band), 5.15–5.825 GHz(high band), 5.925–7.125 GHz(high band) Isolation:23 dB(in low band),22dB (in high band) Antenna Spacing (Edge-to-Edge): 2 mm Method of Mutual Coupling Reduction: Decoupling Inductor (L1) for low band ,Parasitic Branch with Inductor (L2) And Neutralization Line with Inductor (L3) for high band. Antenna Structure: Two identical Inverted-F Antennas (IFAs)
4 | Self-Decoupled 8-Element Dual Polarized MIMO Antenna for B5G Handsets With Sub-6 GHz and mmWave Integration | IEEE ACCESS ,2024 | Operating Frequency: 4.8 GHz,28.5 GHz Isolation:14.4 dB (4.8GHz) and 25 dB(28.5GHz) Method of Mutual Coupling Reduction: Uses two F-shaped slots with independent frequency control for each band and achieves high isolation decoupling through clever orthogonal antenna arrangement. Antenna Structure: 1×2 MPA Array

## Slide 10: Literature (continued):
S.No. | Title of the Paper | Source | Inferences
5 | A Self-Decoupling Method for MIMO Antenna Array Using Characteristic Mode of Ground Plane | IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, 2023 | Operating Frequency: 4GHz Isolation: 57 dB Antenna Spacing (Centre to Centre): 32.8mm(0.44λ ) Method of Mutual Coupling Reduction: The method exploits specific characteristic modes of rectangular ground planes that create two or multiple parallel null-field regions. By strategically placing antenna elements so that one excites the desired mode while others have their feed points located in null-field regions. Antenna Structure: 1 × 2 microstrip patch antenna (MPA) array
6 | Mutual Coupling Reduction in Closely Spaced MIMO Dielectric Resonator Antenna in H-Plane Using Closed Metallic Loop | IEEE ACCESS ,2024 | Operating Frequency: 4.73-5.1 GHz (Sub-6GHz 5G band) Isolation: 28 dB Antenna Spacing (Edge-to-Edge): 1 mm = 0.016λ₀ Method of Mutual Coupling Reduction: Closed metallic loops wrapped around adjacent edges of DRAs, shorted to ground. Antenna Structure: 2×1 MIMO DRA array

## Slide 11: Literature (continued):
S.No. | Title of the Paper | Source | Inferences
7 | Dual-Broadband Aperture-Shared Base Station Antenna Array Using Double Decoupling Techniques | IEEE ACCESS ,2024 | Operating Frequency : Low Band: 1.7-2.5 GHz ;High Band: 3.1-4.1 GHz Isolation : Low Band: >25 dB;High Band: >30 dB Mutual Coupling Reduction Method Double Decoupling Techniques: L-shaped branches - loaded on dipole arms to generate reverse currents Open Ring Decoupling Surface (ODS) - placed above LB antenna for electromagnetic transparency Antenna Structure LB Antenna: Dipole with L-shaped branches + baluns + ODS HB Antennas: 4 antennas (2×1 arrays with power dividers)
8 | Mutual Coupling Reduction Between Two Tightly Packed Half-Split Cylindrical Dielectric Resonator Antennas | IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, 2023 | Operating Frequency: 4.54-5.34 GHz Isolation: 44 dB at 4.9 GHz Antenna Spacing (Edge-to-Edge): 3 mm (0.05λ₀) Method of Mutual Coupling Reduction: Double-sided copper-cladded FR-4 substrate (DS-CCS) insertion & Air gaps on both sides of metal sheet Antenna Structure:Two half-split cylindrical dielectric resonator antennas (CDRAs) .

## Slide 12: Literature (continued):
S.No. | Title of the Paper | Source | Inferences
9 | Mutual Coupling Reduction of a Dual-Band Four-Port Patch Antenna With Co-Polarized Radiation Pattern by Controlling Electric Fields | IEEE TRANSACTIONS ON ANTENNAS AND PROPAGATION, 2023 | Operating Frequency: Dual-band: 2.40 GHz and 3.62 GHz Isolation: >15 dB between all four ports in both bands Method of Mutual Coupling Reduction: Shorting Pins to control mode combinations and electric field nulls Electric field null bending near unexcited ports Ring slots for better impedance matching and bandwidth Antenna Structure: Single-element microstrip patch antenna
10 | Self-Decoupled Dual-Frequency Patch Antennas via Hybrid Coupling Interface Technique | IEEE ANTENNAS AND WIRELESS PROPAGATION LETTERS,2023 | Operating Frequency: 3.77-3.94 GHz Isolation: 15 dB in both bands Antenna Spacing (Edge to Edge): 3 mm (0.039λ) Method of Mutual Coupling Reduction: Hybrid Coupling Interface (HCI) technique Self-decoupling (no external structures) Antenna Structure: Rectangular patch antenna

## Slide 13: Literature (continued):
S.No. | Title of the Paper | Source | Inferences
11 | Design of a Composite Decoupling Structure for Dual-Band Dual-Polarized Base Station Array | IEEE ANTENNAS AND WIRELESS PROPAGATION LETTERS, 2022 | Operating Frequency :B1 Band:3.3-3.7GHz;B2 Band:4.8-5.5 GHz Isolation :B1 Band: >20 dB;B2 Band: >25 dB Antenna Spacing(Edge-to-edge): 0.05λ₁ Mutual Coupling Reduction Method: Composite Decoupling Structure consisting of: DADS (Dual-band Array-antenna Decouple Surface),SDS (Staggered Dielectric Surface),MLR (Meandered Line Resonators) Antenna Structure:Dual-band dual-polarized crossed dipoles
12 | A Wideband Decoupling Technique for Two Inverted-F Antennas Using a Capacitively Loaded Ground Cut | IEEE ANTENNAS AND WIRELESS PROPAGATION LETTERS, 2024 | Operating Frequency Planar MIMO: 2.3-2.8 GHz ;IBFD: 2.36-2.64 GHz ;Vertical: 3.3-3.8 GHz (N78 band) Isolation MIMO: >28-30 dB; IBFD: >40 dB Antenna Spacing (Edge-to-Edge) Planar: ~10-15 mm (estimated from dimensions) Vertical: ~7 mm height separation Method of Mutual Coupling Reduction Capacitively Loaded Ground Cut - Creates two non-resonant coupling paths (M₁ & M₂) that cancel original coupling (M₀) at two frequencies simultaneously Antenna Structure: Inverted-F Antennas (IFAs)

## Slide 14: Literature (continued):
S.No. | Title of the Paper | Source | Inferences
13 | Aperture Fed Microstrip Dual Polarization Wide Scan Phased Array Antenna With Mutual Coupling Reduction | IEEE ACCESS ,2024 | Operating Frequency: 2.77 - 3.10 GHz (S-band) Isolation: >48 dB (between H and V polarizations) Antenna Spacing: Center-to-center: 0.45λ (46.55 mm) Mutual Coupling Reduction Method: Rectangular planar resonators positioned between patch elements Cross-shaped resonator configuration Antenna Structure: Aperture-fed microstrip dual-polarization antenna
14 | Application of Metamaterial Wall for Mutual Coupling Mitigation of a Dual Differential Fed 2 × 2 Patch Array Antenna | IEEE ACCESS ,2024 | Operating Frequency: 9.37 GHz Isolation : >30 dB Antenna Spacing: 0.18λ (edge-to-edge) Mutual Coupling Reduction Method: Double-layer Split Ring Resonator (SRR) metamaterial wall Mechanism: Space wave absorption/blocking Antenna Structure: Array: 2×2 Dual Differential Fed Patch Array (DDFPAA)

## Slide 15: Literature (continued):
S.No. | Title of the Paper | Source | Inferences
15 | Wideband Self-Decoupled Closely Placed Dielectric Patch Antenna Array Without Additional Structures | IEEE ACCESS ,2024 | Operating Frequency: 4.73-5.26 GHz Isolation: >21.5 dB Antenna Spacing (Edge-to-Edge): 2 mm Method of Mutual Coupling Reduction: Wideband Self-Decoupling (no additional structures) Simultaneous excitation of HEM₁₁δ and TE₁₂ modes Antenna Structure: Type: Dielectric Patch Antenna (DPA) Array

## Slide 16: Methodology :
Design and Simulation of a Base Antenna at 2.4 GHz.
Design and Simulation of a Patch antenna array at 2.4 GHz
Design and Simulation of a Patch antenna array with decoupling structures at 2.4 GHz.
Analysis of results and Optimization of design based on the performance parameters
Prototype Fabrication and Measurement

## Slide 17: References:
1)N.-W. Liu, Y.-D. Liang, L. Zhu, G. Fu, Y. Liu, and Y. Yun, “Electric-field null bending of a single dual-port patch antenna for colinear polarization decoupling using characteristic modes analysis,” IEEE Trans. Antennas Propag., vol. 70, no. 12, pp. 12247–12252, Dec. 2022.
2)Q. Xuan Lai, Y. Mei Pan, and S. Yong Zheng, ‘‘Mode-counteraction based self-decoupling in circularly polarized MIMO microstrip patch array,’’ IEEE Trans. Antennas Propag., vol. 70, no. 10, pp. 9337–9346, Oct. 2022.
3)M. Elahi, A. Altaf, E. Almajali, and J. Yousaf, ‘‘Mutual coupling reduction in closely spaced MIMO dielectric resonator antenna in H-plane using closed metallic loop,’’ IEEE Access, vol. 10, pp. 71576–71583, 2022
4)Q. X. Lai, Y. M. Pan, and S. Y. Zheng, ‘‘A self-decoupling method for MIMO antenna array using characteristic mode of ground plane,’’ IEEE Trans. Antennas Propag., vol. 71, no. 3, pp. 2126–2135, Mar. 2023.
5)J. Yin, Y. X. Jia, S. M. Yang, et al., “Design of a composite decoupling structure for dual-band dual-polarized base station array,” IEEE Antennas and Wireless Propagation Letters, vol. 21, no. 7, pp. 1408–1412, 2022.
6)N.-W. Liu, Y.-D. Liang, L. Zhu, Z.-X. Liu, Y. Liu, and S. Sun, “Mutual coupling reduction of a dual-band four-port patch antenna with co-polarized radiation pattern by controlling electric fields,” IEEE Trans. Antennas Propag., vol. 71, no. 5, pp. 4534–4539, May 2023.
7)H. Deng and L. Zhu, “Self-decoupled dual-frequency patch antennas via hybrid coupling interface technique,” IEEE Antennas Wireless Propag. Lett., vol. 22, no. 6, pp. 1256–1260, Jun. 2023.
8)H. Deng and L. Zhu, “Self-decoupled dual-frequency patch antennas via hybrid coupling interface technique,” IEEE Antennas Wireless Propag. Lett., vol. 22, no. 6, pp. 1256–1260, Jun. 2023.

## Slide 18: References:
9)X. Tang, H. Chen, B. Yu, H. Chen, W. Che and Q. Xue, "A Compact Multifrequency Broadband Dual-Antenna System With Mutual Coupling Reduction for Wi-Fi 6E Application," in IEEE Antennas and Wireless Propagation Letters, vol. 23, no. 4, pp. 1296-1300, April 2024
10)W. Tang, J. Sui, J. Li, D. Li and X. Zhu, "A Wideband Decoupling Technique for Two Inverted-F Antennas Using a Capacitively Loaded Ground Cut," in IEEE Antennas and Wireless Propagation Letters, vol. 23, no. 10, pp. 3058-3062, Oct. 2024
11)S. Benny and S. Sahoo, “Aperture fed microstrip dual polarization wide scan phased array antenna with mutual coupling reduction,” IEEE Access, vol. 12, pp. 16397–16407, 2024.
12)K. E. Kedze et al., "Application of Metamaterial Wall for Mutual Coupling Mitigation of a Dual Differential Fed 2×2 Patch Array Antenna," in IEEE Access, vol. 12, pp. 151251-151260, 2024
13)R. Wu, J.-H. Lin, F.-C. Chen, and L. H. Ye, “Dual-broadband apertureshared base station antenna array using double decoupling techniques,” IEEE Antennas Wireless Propag. Lett., vol. 23, pp. 3262–3266, 2024.
14)A. Sufyan, S. A. A. Shah, K. B. Khan, I. A. Shah, A. Ullah, T. A. Siddiqui, S. Islam, and H. Yoo, ‘‘Self-decoupled 8-element dual polarized MIMO antenna for B5G handsets with sub-6 GHz and mmWave integration,’’ IEEE Access, vol. 12, pp. 167324–167332, 2024.
15)L. -L. Yang, X. -F. Wang and J. -X. Chen, "Wideband Self-Decoupled Closely Placed Dielectric Patch Antenna Array Without Additional Structures," in IEEE Access, vol. 12, pp. 140605-140610, 2024

## Slide 19
Thank You